/* hw2.pde */
/* 02/2011 RBH */
/* Arduino 22 */
/* Uses downloaded libraries 'Bounce', 'MemoryFree', 'OneWire', 'glcd' */
/* CPU is AT90USB1286 Teensy++ 2.0 - Used as configured from pjrc.com*/
/* 128k program flash - 8k SRAM - 4k EEPROM */
/* 16MHz external clock */
/* 4/1/2011 - GLCD.print(float, prec) does not work */

/* Solar hot water controller */

#include <SPI.h>
#include <OneWire.h>
#include <EEPROM.h>
#include <Bounce.h>
#include <glcd.h>
#include "fonts/allFonts.h"
#include <glcd_Config.h>
#include "HotWater.h"
#include "MemoryFree.h"
#include <Ethernet.h>
#include <avr/eeprom.h>
#include <Udp.h>

//#define TESTMODE

/* Menu is the data struct that holds the configurable parameters. */
/* Loaded into EEPROM for permanent storage. These numbers are all BYTES */
/* (max 255 and min 0). */
/* desc,min,max,act*/
struct menu EEMEM Menu =
{
    {"Wtr1Hs2Gg3 ", 1, 3, 1}, /* 0 Heat Water (1), House (2), Garage (3) */
    {"Freeze ", 0, 50, 37}, /* 1 Degrees below freezing before pump on */
    {"UseTank1 ", 0, 1, 1}, /* 2 use 1 or don't use 0 this tank */
    {"UseTank2 ", 0, 1, 1}, /* 3 use 1 or don't use 0 this tank */
    {"MaxTankTemp", 120, 180, 165},/*4 max tank temp - applies to both tanks */
    {"TempDiffMax", 10, 24, 18}, /* 5 turn on temp diff between collectr & tnk */
    {"TempDiffMin", 3, 10, 5}, /* 6 min temp diff between collector and tank */
    {"HeatEnable ", 0, 2, 2}, /* 7 1-house heat on. 0-house heat off. */
        /* 2-auto - input from house thermostat */
    {"DumpTimeHr ", 0, 23, 16}, /* 8 hour when to dump collector to dump */
        /* device - house or garage */
    {"DumpTimeMin", 0, 59, 15}, /* minute for dump time */
    {"ZoneOffTime", 0, 30, 20}, /* time in minutes to keep a zone valve */
        /* open after the pump turns off */
    {"SensorErrTh", 0, 254, 10}, /* sensor error cnt threshold before */
        /* sounding the buzzer - 0 is off */
    {"EndSwtchSec", 10, 60, 35}, /* number of seconds to wait for the zone */
        /* valve end switch to close before alarm */
    {"BeepEnable ", 0, 1, 1}, /* Beep on or off */
    {"NTPTimeFlag ", 0, 1, 1}, /* 1=get unixtime from NTP server; 0=no */
    {"IPport ", 1, 255, 6}, /* port to listen on for connections. */
    {"IPAddress1 ", 0, 255, 192},
    {"IPAddress2 ", 0, 255, 168},
    {"IPAddress3 ", 0, 255, 5},
#ifdef TESTMODE
    {"IPAddress4 ", 0, 255, 33},
#else
    {"IPAddress4 ", 0, 255, 32},
#endif
#ifdef TESTMODE
    {"MACAddress1 ", 0, 255, 255},
#else
    {"MACAddress1 ", 0, 255, 222},
#endif
    {"MACAddress2 ", 0, 255, 222},
    {"MACAddress3 ", 0, 255, 222},
    {"MACAddress4 ", 0, 255, 222},
    {"MACAddress5 ", 0, 255, 222},
    {"MACAddress6 ", 0, 255, 224},
    {"DftGateway1 ", 0, 255, 192},
    {"DftGateway2 ", 0, 255, 168},
    {"DftGateway3 ", 0, 255, 5},
    {"DftGateway4 ", 0, 255, 1},
    {"SubnetMask1 ", 0, 255, 255},
    {"SubnetMask2 ", 0, 255, 255},
    {"SubnetMask3 ", 0, 255, 255},
    {"SubnetMask4 ", 0, 255, 0},
    {"NTPIPAddress1", 0, 255, 96}, /* Bridgewater NJ */
    {"NTPIPAddress2", 0, 255, 47},
    {"NTPIPAddress3", 0, 255, 67},
    {"NTPIPAddress4", 0, 255, 105}
};

/* desc, state, pin */
struct stat CurrStatus =
{
    {"Manual ", 0, 0},
    {"Tank1 ", 0, TANK1_PIN},
    {"Tank2 ", 0, TANK2_PIN},
    {"House ", 0, HOUSE_PIN},
    {"Garage ", 0, GARAGE_PIN},
    {"Pump ", 0, PUMP_PIN},
    {"PumpGarage", 0, PUMP_GARAGE_PIN},
    {"Stiebel ", 0, STIEBEL_PIN}
};
struct stat PrevStatus;

/* If the order of screens changes in this array */
/* then change ConfigParam() */
struct screens Screens[NUM_SCREENS] = {
    {"MainScreen", MainScreen},
    {"Config Param", ConfigParam},
    {"Manual", Manual},
    {"SensorConfig1", SensorConfig1},
    {"SensorConfig2", SensorConfig2},
    {"FreeRAMBytes", FreeRAM}
};

/* Temp sensor data structures */
/* SensorsEE is the sensor data that does not change. It's loaded into */
/* EEPROM using avrdude after Arduino uploads the program into flash memory. */

#ifdef TESTMODE
struct sensorsEE EEMEM SensorsEE =
{
    {0x28,0x9B,0xBB,0xBA,0x02,0x00,0x00,0xAD, "Collector"},
    {0x28,0x17,0x82,0x5E,0x02,0x00,0x00,0x0A, "T1Top "},
    {0x28,0xCF,0xC7,0x5E,0x02,0x00,0x00,0x54, "T1Bot "},
    {0x28,0x7A,0xA4,0x5E,0x02,0x00,0x00,0xE7, "T2Top "},
    {0x28,0x9D,0x9A,0x5E,0x02,0x00,0x00,0x6D, "T2Bot "},
    {0x28,0x83,0x9E,0x5E,0x02,0x00,0x00,0x3A, "Ambient "}
}; /* the sensors on the bench */
#else
struct sensorsEE EEMEM SensorsEE =
{
    {0x28,0xD8,0xBD,0xBA,0x02,0x00,0x00,0x1D, "Collector"},
    {0x28,0x8D,0x67,0x9E,0x01,0x00,0x00,0xA1, "T1Top "},
    {0x28,0x7E,0x55,0x9E,0x01,0x00,0x00,0x8D, "T1Bot "},
    {0x28,0x56,0x4C,0x9E,0x01,0x00,0x00,0x15, "T2Top "},
    {0x28,0x7E,0x58,0x9E,0x01,0x00,0x00,0x61, "T2Bot "},
    {0x28,0x6C,0xB0,0xBA,0x02,0x00,0x00,0x2A, "Ambient "}
};
#endif

/* Temp Sensor temperature readings */
struct TempSensor TSdata[NUM_DS18B20];
struct hist_item History[NUM_HISTORY_RECS];
struct message Msg[NUM_MSG];

OneWire ds1(DSTEMP1_PIN);
OneWire ds2(DSTEMP2_PIN);
boolean ReadTempFlag = false;
boolean BuzzerState = false;
boolean BeepState = false;

boolean ZoneValveEndSwitch = false;
byte ZoneValveEndSwitchTimer = 0;
int ZoneTimerCnt = 0;
boolean CollectorTooHotFlag = false;
byte CollectorTooHotTimer = 0;
boolean HeatEnabled = false;
boolean DumpFlag = false;

/* TurnOnTemp used in temp display func and Calc() */
float TurnOnTemp;

/* The active zone valve pin. Global so calc and the screen func can get it */
byte ActiveZonePin;

byte BackLightTimer = 0;
boolean BallTimerFlag = false;

time_t UnixTime = 0UL;
struct mytime hwtime;
boolean UnixTimeIsGood = false;
boolean NTPRequestPending = false;

byte CurScreenIdx = 0, MenuTimerCnt = 0;

Bounce dbBackSwitch = Bounce(BACKBUTTONPIN, 40);
Bounce dbUpSwitch = Bounce(UPBUTTONPIN, 40);
Bounce dbDnSwitch = Bounce(DNBUTTONPIN, 40);
Bounce dbSaveSwitch = Bounce(SAVEBUTTONPIN, 40);
//Bounce dbHeatEnabled = Bounce(HeatEnabledPin, 30);
Bounce dbZoneValveEndSwitch = Bounce(ZoneValveEndSwitchPin, 30);

Server server((int)GetEEact(IP_PORT_LOC));

void setup()
{
    byte sensorcnt, readingnum;

    pinMode(WIZRESET_PIN, OUTPUT);
    pinMode(BACKLIGHT_PIN, OUTPUT);
    pinMode(BUZZER_PIN, OUTPUT);
    pinMode(PUMP_PIN, OUTPUT);
    pinMode(PUMP_GARAGE_PIN, OUTPUT);
    pinMode(TANK1_PIN, OUTPUT);
    pinMode(TANK2_PIN, OUTPUT);
    pinMode(HOUSE_PIN, OUTPUT);
    pinMode(GARAGE_PIN, OUTPUT);
    pinMode(STIEBEL_PIN, OUTPUT);
    pinMode(LED_PIN, OUTPUT);

    pinMode(UPBUTTONPIN, INPUT);
    digitalWrite(UPBUTTONPIN, HIGH);
    pinMode(DNBUTTONPIN, INPUT);
    digitalWrite(DNBUTTONPIN, HIGH);
    pinMode(SAVEBUTTONPIN, INPUT);
    digitalWrite(SAVEBUTTONPIN, HIGH);
    pinMode(BACKBUTTONPIN, INPUT);
    digitalWrite(BACKBUTTONPIN, HIGH);

    pinMode(HeatEnabledPin, INPUT);
    digitalWrite(HeatEnabledPin, HIGH);
    pinMode(ZoneValveEndSwitchPin, INPUT);
    digitalWrite(ZoneValveEndSwitchPin, HIGH);

    StartWiznet();
    GLCD.Init();
    GLCD.ClearScreen();
    GLCD.SelectFont(System5x7, BLACK);
    BackLight(BACKLIGHT_FULL);
    SetupForNewScreen();

    memset(TSdata, 0, sizeof(TSdata));
    memset(History, 0, sizeof(History));
    memset(Msg, 0, sizeof(Msg));
    memset(&PrevStatus, 0, sizeof(PrevStatus));

    for(sensorcnt=0; sensorcnt < NUM_DS18B20; sensorcnt++)
        for(readingnum=0; readingnum < NUM_TEMP_READINGS; readingnum++)
        TSdata[sensorcnt].temp[readingnum] = 999;
    delay(500);
    if(GetEEact(NTP_TIME_FLAG_LOC))
        sendNTPpacket(); /* request NIST time */
}

void loop()
{
    static byte sensor_cnt = 0, level = 0, err_cnt;
    static boolean startflg = true;
    static boolean tempsgood = false;
    struct sensorEE ssEE;
    OneWire *dsptr;
    float temp;
    byte ret;

    if(!CheckEEPROM())
        return;
    if(ReadTempFlag) /* no need to do these things w/every loop */
    {
        dbZoneValveEndSwitch.update();
        ZoneValveEndSwitch = !dbZoneValveEndSwitch.read(); /* active low */

        if(GetEEact(HEAT_ENABLED_LOC) == 2)
        {
        //dbHeatEnabled.update();
        //HeatEnabled = !dbHeatEnabled.read(); /* active low */
        if(analogRead(HeatEnabledPin) < 512)
        HeatEnabled = true;
        else
        HeatEnabled = false;
        }
        else
        {
        if(GetEEact(HEAT_ENABLED_LOC) == 0)
        HeatEnabled = true;
        else
        HeatEnabled = false;
        }
    }

    /* level 0 = new screen w/just heading */
    /* level 1 = heading + parameter name */
    /* level 2 = heading + parameter + parameter options */
    /* level 3 = all of above plus save button pressed after level 2 */
    /* save button advances to new levels except level 3 = save */
    /* back button goes back levels */
    /* up and down buttons on level 0 inc and decrement the */
    /* thermostat temp setting */
    /* the back button on level 0 goes thru the screens */

    if(dbUpSwitch.update())
        if(dbUpSwitch.read() == false) /* Active low. */
        {
        BackLight(BACKLIGHT_FULL);
        (*Screens[CurScreenIdx].ScreenFunc)(level, UPBUTTONPIN);
        }
    if(dbDnSwitch.update())
        if(dbDnSwitch.read() == false) /* Active low. */
        {
        BackLight(BACKLIGHT_FULL);
        (*Screens[CurScreenIdx].ScreenFunc)(level, DNBUTTONPIN);
        }
    if(dbBackSwitch.update())
        if(dbBackSwitch.read() == false)
        {
        BackLight(BACKLIGHT_FULL);
        if(level == 0)
        {
        if(++CurScreenIdx == NUM_SCREENS)
        CurScreenIdx = 0;
        SetupForNewScreen();
        }
        else
        {
        if(level > 0)
        level--;
        if(level == 0)
        {
        CurScreenIdx = 0;
        SetupForNewScreen();
        }
        (*Screens[CurScreenIdx].ScreenFunc)(level, BACKBUTTONPIN);
        }
        }
    if(dbSaveSwitch.update())
        if(dbSaveSwitch.read() == false) /* Active low. */
        { /* special level = 3 for SAVE when prev level is 2 */
        BackLight(BACKLIGHT_FULL);
        if(level < 3)
        level++;
        (*Screens[CurScreenIdx].ScreenFunc)(level, SAVEBUTTONPIN);
        if(level == 3)
        level = 2;
        }

    /* ReadTempFlag is true once every 200ms. Startflag is true when a temp */
    /* conversion can be done on the next sensor. You need to start a temp */
    /* conversion and wait about 750ms for the conversion to finish in the */
    /* sensor. startflag is true when the data is read from a sensor. */
    /* The next sensor is selected and command sent to start the conversion */
    if(ReadTempFlag || startflg)
    {
        GetEEsensor(sensor_cnt, &ssEE);
        if(sensor_cnt == COLLECTOR_LOC)
        dsptr = &ds1;
        else
        dsptr = &ds2;
        if(startflg)
        {
        StartTemp(dsptr, ssEE.addr);
        err_cnt = 0;
        startflg = false;
        }
        else
        {
        /* GetTemp returns 0 if sensor not ready yet */
        /* 1 if a failure or 2 if OK */
        temp = 0.0;
        ret = GetTemp(dsptr, ssEE.addr, &temp);
        if(ret == 2) /* OK */
        {
byte readingcnt, totcnt=0;
        float tot;

        for(readingcnt=0; readingcnt<NUM_TEMP_READINGS-1; readingcnt++)
        {
        if(TSdata[sensor_cnt].temp[readingcnt] != 999)
        {
        tot += TSdata[sensor_cnt].temp[readingcnt];
        totcnt++;
        }
        TSdata[sensor_cnt].temp[readingcnt] =
        TSdata[sensor_cnt].temp[readingcnt+1];
        }
        tot += temp;
        totcnt++;
        TSdata[sensor_cnt].temp[NUM_TEMP_READINGS-1] = temp;
        TSdata[sensor_cnt].avgtemp = tot/totcnt;

        startflg = true;
        if(++sensor_cnt >= NUM_DS18B20)
        {
        sensor_cnt = 0;
        tempsgood = true;
        }
        }
        /* sensor not done with temp A2D conversion yet(0) or failure (1) */
        if(ret == 0 || ret == 1)
        err_cnt++;
        /* If it takes too long for the temp conversion or too many failures */
        if(err_cnt >= 10) /* forget this sensor and move on */
        {
        if(++TSdata[sensor_cnt].failcnt == 255)
        TSdata[sensor_cnt].failcnt = 1;
        if(TSdata[sensor_cnt].failcnt > GetEEact(SENSOR_ERR_TH_LOC) && GetEEact(SENSOR_ERR_TH_LOC) > 0)
        {
        BuzzerState = true;
        AddMsg("SensorFail", ssEE.location);
        }
        startflg = true;
        if(++sensor_cnt >= NUM_DS18B20)
        sensor_cnt = 0;
        }
        }
    }

    /* When a temp is updated and the temp display screen is active */
    /* then update the display. */
    if(startflg)
    {
        (*Screens[0].ScreenFunc)(NULL, NULL);
        if(MenuTimerCnt == 0)
        level = 0; /* Need this here in case the menu times out */
    }

    /* startflg is true after a temp reading. */
    if((tempsgood && startflg) || CurrStatus.Manual.state == 1)
    {
        CheckTooHot();
        if(!CollectorTooHotFlag && CurrStatus.Manual.state == 0)
        CalcHotWater();
        UpdateOutputs();
    }
    if(GetEEact(NTP_TIME_FLAG_LOC))
    {
        time_t ret;
        ret = ntp_get();
        if(ret > 0)
        {
        char t[MSG_LENGTH];
        UnixTime = ret;
        ltoa(ret, t, 10);
        AddMsg("Set Time", t);
        UnixTimeIsGood = true;
        }
    }
    ProcessServerRequest();
    OneSecTimer();
    if(BallTimerFlag && tempsgood)
        MoveBall();
}

/* Write the state of the outputs to the pins. If anything in the CurrStatus */
/* struct changes then make a history record and beep. */
void UpdateOutputs()
{
    byte offset, num_items;
    struct output *outptr, *prevptr;

    num_items = sizeof(struct stat)/sizeof(struct output);
    /* Skip over manual mode which is offset 0 */
    for(offset = 1; offset < num_items; offset++)
    {
        outptr = (struct output *)&CurrStatus + offset;
        digitalWrite(outptr->pin, outptr->state);
    }

    if(memcmp(&PrevStatus, &CurrStatus, sizeof(struct stat)) != 0)
    {
        SaveHistory();
        memcpy(&PrevStatus, &CurrStatus, sizeof(struct stat));
        BeepState = true;
    }
}

/* OneSecTimer() */
/* This is called every time in the loop() function */
/* Sets and unsets flags for various timer variables and flags */
void OneSecTimer()
{
    static unsigned long readflg_millis = 0UL;
    static unsigned long sec_millis = 0UL;
    static unsigned long buzzer_millis = 0UL;
    static unsigned long beep_millis = 0UL;
    static unsigned long ball_millis = 0UL;
    static unsigned long msg_millis = 0UL;
    unsigned long cur_millis;
    static byte dutycycle = 0;

    cur_millis = millis();
    if(cur_millis - readflg_millis >= 200UL)
    {
        ReadTempFlag = true;
        readflg_millis = cur_millis;
    }
    else
        ReadTempFlag = false;

    if(cur_millis - ball_millis > 150UL)
    {
        BallTimerFlag = true;
        ball_millis = cur_millis;
    }

    /* every second */
    if(cur_millis - sec_millis >= 1000UL)
    {
        sec_millis = cur_millis;

        if(MenuTimerCnt > 0)
        MenuTimerCnt--;
        if(MenuTimerCnt == 1)
        {
        if(CurScreenIdx != 0)
        {
        CurScreenIdx = 0;
        SetupForNewScreen();
        }
        }
        /* Zone valve end switch should close in x minutes or failure */
        if(ZoneValveEndSwitchTimer > 0)
        ZoneValveEndSwitchTimer--;

        if(CollectorTooHotTimer > 0)
        CollectorTooHotTimer--;

        UnixTime++;
        SetTime(); /* fill the hwtime struct */

        /* Every 12 hours get the NTP time */
        if(UnixTime % 43200 == 0 && GetEEact(NTP_TIME_FLAG_LOC))
        sendNTPpacket(); /* request NIST time */

        /* Every 5 minutes make a history record */
        if(UnixTime % 300 == 0)
        SaveHistory();

        /* Every minute */
        if(UnixTime%60 == 0)
        {
        /* Turn zone off if not used for x minutes */
        if(ZoneTimerCnt > 0)
        ZoneTimerCnt--;

        if(BackLightTimer == 0)
        BackLight(BACKLIGHT_HALF);
        if(BackLightTimer > 0)
        BackLightTimer--;
        }
    }

    /* Now do the buzzer and beep */
    if(cur_millis - buzzer_millis >= 500)
    {
        if(dutycycle == 0 && BuzzerState)
        dutycycle = 125;
        else
        dutycycle = 0;
        buzzer_millis = cur_millis;
    }
    if(BeepState && !BuzzerState && dutycycle == 0 && GetEEact(BEEP_ENABLE_LOC) == 1)
    {
        dutycycle = 100;
        beep_millis = cur_millis;
    }
    if(cur_millis - beep_millis > 80ul && BeepState)
    {
        dutycycle = 0;
        BeepState = false;
    }
    analogWrite(BUZZER_PIN, dutycycle);
}

void SaveHistory()
{
    byte x;

    /* bump all recs to the front of the array */
    for(x=0; x<NUM_HISTORY_RECS-1; x++)
        memcpy(&History[x], &History[x+1], sizeof(struct hist_item));

    History[NUM_HISTORY_RECS-1].unixtime = UnixTime;
    memcpy(&History[NUM_HISTORY_RECS-1].TS, &TSdata, sizeof(TSdata));
    memcpy(&History[NUM_HISTORY_RECS-1].CS, &CurrStatus, sizeof(CurrStatus));
}