/* hw2.h rbh 02/2011 */

typedef unsigned long time_t;

#define NUM_SCREENS 6
#define MENU_ON_SECONDS 30
#define BACKLIGHT_TIMER_MIN 2
#define NUM_DS18B20 6
#define NUM_DS18B20_ADDRESS_BYTES 8
#define NUM_IP_ADDRESS_BYTES 4
#define NUM_MAC_ADDRESS_BYTES 6
#define NUM_HISTORY_RECS 10
#define NUM_TEMP_READINGS 10
#define NUM_MSG 10 /* number of msg */
#define MSG_LENGTH 11
#define STIEBEL_TEMP_START 107

#define NTP_PACKET_SIZE 48
#define NTP_UDP_PORT 8888

/* Offsets into the Menu->item structure in EEPROM */
#define WTR1HS2GG3_LOC 0
#define FREEZE_LOC 1
#define USE_TANK1_LOC 2
#define USE_TANK2_LOC 3
#define MAX_TANK_TEMP_LOC 4
#define TEMP_DIFF_MAX_LOC 5
#define TEMP_DIFF_MIN_LOC 6
#define HEAT_ENABLED_LOC 7
#define DUMP_TIME_HR_LOC 8
#define DUMP_TIME_MIN_LOC 9
#define ZONE_OFF_TIMER_LOC 10
#define SENSOR_ERR_TH_LOC 11
#define END_SWTCH_SEC_LOC 12
#define BEEP_ENABLE_LOC 13
#define NTP_TIME_FLAG_LOC 14
#define IP_PORT_LOC 15
#define IP_ADDRESS1_LOC 16
#define MAC_ADDRESS1_LOC 20
#define DFT_GATEWAY1_LOC 26
#define SUBNET_MASK1_LOC 30
#define NTP_IP_ADDRESS1_LOC 34

/* Offsets into the SensorsEE struct in EEPROM */
#define COLLECTOR_LOC 0
#define T1TOP_LOC 1
#define T1BOT_LOC 2
#define T2TOP_LOC 3
#define T2BOT_LOC 4
#define AMBIENT_LOC 5

char colon = ':'; /* Used primarily in server.pde */

/* Definitions for the graphics on the display */
#define GARAGE_WIDTH 9
#define TANK1_WIDTH 33
#define TANK2_WIDTH 33
#define HOUSE_WIDTH 9
#define COLLECTOR_WIDTH 34

#define GARAGE_X_POS 0
#define TANK1_X_POS GARAGE_WIDTH+2
#define TANK2_X_POS TANK1_X_POS+TANK1_WIDTH+2
#define HOUSE_X_POS TANK2_X_POS+TANK2_WIDTH+2
#define COLLECTOR_X_POS HOUSE_X_POS+HOUSE_WIDTH+2

#define ZONE_Y_POS 10
#define ZONE_HEIGHT 28
#define COLLECTOR_HEIGHT ZONE_HEIGHT/2

/* PWM LCD backlight brightness */
#define BACKLIGHT_OFF 0
#define BACKLIGHT_HALF 70
#define BACKLIGHT_FULL 255

struct TempSensor {
    float avgtemp;
    float temp[NUM_TEMP_READINGS];
    byte failcnt;
};

struct sensorEE {
    byte addr[NUM_DS18B20_ADDRESS_BYTES];
    char location[10];
};

struct screens {
    char *ScreenName;
    void (*ScreenFunc)(byte, byte);
};

/* Informational message displayed on the display */
struct message {
    char line1[MSG_LENGTH+1];
    char line2[MSG_LENGTH+1];
    int cnt;
};

struct sensorsEE {
    struct sensorEE Collector;
    struct sensorEE T1Top;
    struct sensorEE T1Bot;
    struct sensorEE T2Top;
    struct sensorEE T2Bot;
    struct sensorEE Ambient;
};

struct item {
    char desc[14];
    byte min;
    byte max;
    byte act;
};

struct output {
    char desc[11];
    byte state;
    byte pin;
};

/* The pumps must be after the zones in the structure. */
/* The loops in CalcHotWater depends on the zones being */
/* done before the pumps. */
/* Manual must be at the 0 position and Stiebel the last. */
struct stat {
    struct output Manual;
    struct output Tank1;
    struct output Tank2;
    struct output House;
    struct output Garage;
    struct output Pump;
    struct output PumpGarage;
    struct output Stiebel;
};

struct hist_item {
    time_t unixtime;
    struct TempSensor TS[NUM_DS18B20];
    struct stat CS;
};

struct mytime {
    byte sec; /* Seconds [0,60] */
    byte min; /* Minutes [0,59] */
    byte hour; /* Hour [0,23] */
    byte mday; /* Day of month [1,31] */
    byte month; /* Month of year [1,12] */
    int year; /* Years since 1900 */
    byte wday; /* Day of week [1,7] Sunday =1 */
    byte isdst; /* Daylight Savings flag */
};

struct menu {
    struct item Wtr1Hs2Gg3;
    struct item Freeze;
    struct item UseTank1;
    struct item UseTank2;
    struct item MaxTankTemp;
    struct item TempDiffMax;
    struct item TempDiffMin;
    struct item HeatEnable;
    struct item DumpTimeHr;
    struct item DumpTimeMin;
    struct item ZoneOffTimer;
    struct item SensorErrTh;
    struct item EndSwtchSec;
    struct item BeepEnable;
    struct item NTPTimeFlag;
    struct item IPport;
    struct item IP1;
    struct item IP2;
    struct item IP3;
    struct item IP4;
    struct item MAC1;
    struct item MAC2;
    struct item MAC3;
    struct item MAC4;
    struct item MAC5;
    struct item MAC6;
    struct item DftGateway1;
    struct item DftGateway2;
    struct item DftGateway3;
    struct item DftGateway4;
    struct item SubnetMask1;
    struct item SubnetMask2;
    struct item SubnetMask3;
    struct item SubnetMask4;
    struct item NTPIP1;
    struct item NTPIP2;
    struct item NTPIP3;
    struct item NTPIP4;
};

/* Pin Inputs */
#define UPBUTTONPIN 2
#define DNBUTTONPIN 3
#define SAVEBUTTONPIN 4
#define BACKBUTTONPIN 5
#define HeatEnabledPin 38
#define ZoneValveEndSwitchPin 1

/* Pin outputs */
#define BACKLIGHT_PIN 0
#define LED_PIN 6
#define WIZRESET_PIN 24
#define DSTEMP1_PIN 25 /* Collector Temp Sensor */
#define DSTEMP2_PIN 26 /* Tank Sensors */
#define BUZZER_PIN 27
#define PUMP_PIN 45
#define PUMP_GARAGE_PIN 44
#define TANK1_PIN 43
#define TANK2_PIN 42
#define HOUSE_PIN 41
#define GARAGE_PIN 40
#define STIEBEL_PIN 39